## Slide 1
STS-Vision
Camera Pose Ground Truth Tool
Jorge Enriquez
Mentors:
Philip Bailey, Tu-Hoa Pham
Jet Propulsion Laboratory, California Institute of Technology
Pre-Decisional Information – For Planning and Discussion Purposes Only
Reviewed and determined not to contain CUI

## Slide 2: Abstract
Ground Truth is often acquired through external means (Vicon balls, April tags)
The Ground Truth Tool (GTT) allows ground truth to be generated in otherwise unreliable or unattainable circumstances.
Allows 2D selection of points, which are fed into a Perspective N Point algorithm

## Slide 3: Bio
Graduated CSU Northridge
  B.S in Computer Science
Undergraduate Research Assistant
  Image Classification using EfficientNet, DaVit, MobileOne
Compiler for Hierarchical State Machine language (Proteus)

## Slide 4: Acronyms [1]
PnP: Perspective N Point
  Algorithm that takes a subset of 2d points in the image, 3d points in the world, and a camera model, calculating a best fit camera position that allows those rays to coincide
RANSAC: Random Sample Consensus
  Sampling method that randomly selects a small subset of 2d points, just large enough to run PnP (about 3 points)
  Creates a model and checks how many inliers fit in the estimated model.
  Iterates over a parametrized number (10,000)
Inliers / Outliers
  After calculating a camera pose, all 3d test coordinates are reprojected into the image such and compared to their corresponding 2d coordinate
  The error in pixels between the resulting projected 2d point and the original input 2d point is compared against a parameterizable reprojection error defined in pixels.
  Points that have a delta of less than the reprojection error are considered Inliers, and the rest are considered Outliers

## Slide 5: Acronyms [2]
TSM: Template Synthesis (and) Matching
  The current primary localization algorithm for SRL’s STS Vision System that takes in a 3d model, renders an image of said model in the expected current pose relative to the camera, then locally searches for predefined patches (templates) from the rendered image in a larger area in the test image
  Template 2d coordinates on the rendered image, have a corresponding 3d depth value provided by the renderer. These 2d (Test Image) to 3d (Rendered Image) correspondences are fed to PnP to generate a pose

## Slide 6: Overview [1]
TSM works on simulated images incredibly well
Pose Error:
  0.009 mm Normal Translational
  0.09 mm Lateral Translational
  0.1 mrad in-plane rotation
  1 mrad out-of-plane rotation
Notes: Normal – Perpendicular to the axis o

## Slide 7: Overview [2]
TSM on Douglass Dock visually runs well, however, with respect to the ground truth, shows large margin of error
Pose Error:
  2 mm Normal Translation
  5.3 mm Lateral Translation
  2.2 mrad in-plane rotation
  9.3 mrad out of plane rotation
Notes: Normal – Perpendicular to the axis o

## Slide 8: Design [1]
Notes: First Design

## Slide 9: Design [2]
Notes: First Design with Functionality

## Slide 10
Design [3]
Notes: Current Design

## Slide 11: Features [1]
Render Images
If a rasterizer tool is present, GTT can send commands to generate image
Rendered Image can be toggled, displaying the original image and the rendered image like a gif.
Rendered Image is automatically saved with original image

## Slide 12: Features [2]
Slider Tool
Takes two images and overlays them in a way that a slider can blend seamlessly
Needs rasterizer to produce a rendered image if utilized within the GTT
Can run independently
Pre-Decisional Information – For Planning and Discussion Purposes Only
Reviewed and determined not to contain CUI

## Slide 13: Features [3]
Save Files
Saves points (Reference, Test, Projected)
Saves the transformation matrix generated by PnP
Saves the current canvas on display

## Slide 14: Results [1]
0.3 mm normal error; 2 mm lateral; 28 mrad in out of plane
Another round of testing with more points and lower reprojection error threshold is warranted
Douglass
Mars 2020
Due to the close FOV of the camera, points bunch up, introducing bias
Images with a farther FOV lack the quality to correctly quantify error
Reviewed and determined not to contain CUI

## Slide 15: Results [2]
Hi-Fidelity Douglass
Reviewed and determined not to contain CUI

## Slide 16: Whats next
Get a job!
  Computer Vision
  ML / AI
  Compilers
Study for the GRE
Get Masters
???
Return to JPL!
Reviewed and determined not to contain CUI

## Slide 17: Thank You!
Special Thanks
Phil Bailey
Tu-Hoa Pham
Philip Twu
Todd Litwin
Austin Kwon
Federico Pizarro
And to everyone else, Thank You!
Reviewed and determined not to contain CUI

## Slide 18
Reviewed and determined not to contain CUI

## Slide 19: Prerequisites
Perspective N Point
Camera Matrix:
3D Points (w/r the world):
2D Points (w/r the frame):
Rotation / Translation Matrix:
Pinhole Camera
Given by CAD Model (3D Reference Points)
Given by GTT (2D Test Points)
Goal
Reviewed and determined not to contain CUI

## Slide 20: Requirements
Reviewed and determined not to contain CUI
Notes: Normal – Perpendicular to the axis o

## Slide 21: Other Images
Reviewed and determined not to contain CUI

## Slide 22: Other Images
Reviewed and determined not to contain CUI